## Slide 1
SIGNALS AND SYSTEMS USING MATLAB
Chapter 0 — From the Ground Up!
L. F. Chaparro and A. Akan

## Slide 2: Digital signal processing
1948 – birth of digital technologies
  Transistor (Bell Labs)
  Stored–program computer (Manchester University, UK)
  Publications
    Shannon’s digital communications
    Hamming’s error correcting codes
    Wiener’s Cybernetics
Moore’s Law, DSPs and FPGs
  1965 — Moore (Intel): number of transistors in a chip would double every 2 years
  Digital Signal Processors (DSPs): optimized microprocessors for real–time processing
  Field Programmable Gate Array (FPGA): device with programmable blocks and interconnects

## Slide 3: Compact disc (CD) and compact disc player
DAC
Laser
Sensor
Audio Amplifier
Speaker
When playing a CD, the CD player follows tracks in the disc, focus laser beam on them, as CD is spun. Light is reflected by pits and bumps on the surface of disc (corresponding to the coded digital signal from acoustic signal). Sensor detects reflected light and converts it into a digital signal and converted into an analog signal by DAC. Amplified and fed to speakers signal sounds like original recorded acoustic signal.

## Slide 4: Software–defined radio (SDR)
ADC
Modulator
DAC
Super heterodyne
ADC
Demodulator
DAC
Microphone
Antenna
Antenna
Speaker
TRANSMITTER
RECEIVER
Voice SDR mobile two-way radio
Transmitter: voice signal inputted using microphone, amplified by an audio amplifier, converted into a digital signal by ADC,modulated using software, converted by DAC into analog signal which is amplified and radiated by antenna
Receiver: analog signal received by antenna is processed by a superheterodyne, converted by ADC,demodulated using software, converted by DAC, amplified and fed to speaker

## Slide 5: Computer–control system
Digital Computer
DAC
Plant
ADC
r(t) +
-
Clock | 
 | Sensor
w(t)
y(t)
v(t)
Computer control system for an analog plant (e.g., cruise control for a car) Reference signal r (t) (e.g., desired speed) and output y (t) (e.g., car speed)
Signals v (t) and w(t): disturbances or noise in plant and sensor (e.g., electronic noise in the sensor and undesirable vibration in the car)

## Slide 6: Continuous and discrete representations
0
1
2
3
4
5
6
7
8
9
10
0
−2
Sampling continuous–time signal x (t) into discrete–time signal sequence x [n]:
x [n] = x (nTs ) = x (t)|t=nTs
Ts :sampling perioddepends on frequency content of x (t)
2
1
x (0.1n)
0
1
2
3
4
6
7
8
9
10
2
0
−2
5
t (sec)
2
x (n)
Sampling x (t) = 2 cos(2πt), 0 ≤ t ≤ 10, with Ts1 = 0.1 (top) and Ts2 = 1 (bottom) giving x1(0.1n) = x1[n] and x2(n) = x2[n]
Notice similarity between x1[n] and x (t) and loss of information when Ts2 = 1

## Slide 7: Inherent discrete–time signal
260
240
220
200
180
160
140
120
100
20 40 60 80 100 120 140
Week
Dollars
ACM Closings, Jan. 2006− Dec. 2009
Weekly closings of ACM stock for 160 weeks in 2006 to 2009. ACM is the trading name of the stock of the imaginary company ACME Inc. makers of everything you can imagine.

## Slide 8: Implementation of DSP Algorithms
Continuous-time signals Electrical and electronic circuits
Digital signals Addition, multiplication, and delay
DSP system’s output Arithmetic operations on input
Possible real-time implementations;
  General-purpose microprocessors (Ps) and micro-controllers (Cs)
  General-purpose digital signal processors (DSPs)
  Field programmable gate arrays (FPGAs)

## Slide 9: Infinitesimal and finite calculus
Derivative and forward– difference
Integral and summation

## Slide 10: Approximation of integral
0
2
4
6
8
10
10
8
6
4
2
0
t
t, n
 |  |  |  | t |  |  |  |  |  | 

## Slide 11: Differential and difference equations
Solve d.e. from series RC circuit with a constant voltage source vi (t) as input and R = 1 Ω, C = 1 F (huge plates!)
c
dv (t)
dt
t ≥ 0
vi (t) = vc (t) +
with initial voltage vc (0) across capacitor
Use integrators
vi(t)
vc(t)
vc(t)
dvc(t)
dt
dvc(t)
dt
d(.)
dt
(.)dt
+
vi(t)
+
vc(0)
Block diagram for d.e. using differentiators (left) and integrators (right). Differentiators increase noise, integrators smooth out noise

## Slide 12
t t0 t1
∆t
Trapezoidal approximation of area
Difference equation
c
v (nT ) =
T
2 + T
[vi (nT ) + vi ((n − 1)T )] +
2 − T
2 + T
c
v ((n − 1)T ),
c
v (0) = 0, n ≥ 1
can be solved iteratively

## Slide 13: Complex or real?
Damping and frequencyof signals represented by complex variable
Complex numbers and functions
(x, y)
|z|
θ
x
y
z
v
z + v
(x, y)
(x, −y)
|z|
θ
θ
|z|
(a)
(b)
(c)
(d)
z
v
|v|
|z||v|
|z|
θ
φ
θ + φ
(a) z = x + jy as vector ; (b) addition of complex numbers; (c) multiplication of complex numbers; (d) complex conjugation of z.

## Slide 14: Complex numbers
Representations
z = x + jy
j ∠z
= |z |e
rectangular polar
Operations
z = 3 + j4 = 5ej0.93
u = −3+ j = √10 ej2.82
j3.79
w = −4 − 3j = 5 e
v = 1 − j = √2 e−jπ/4
3
3
1
1
1
4
3
Re[z]
Re[z]
Re[z]
Re[z]
Im[z]
Im[z]
Im[z]
Rectangular to polar conversion

## Slide 15: Euler’s identity
ej θ = cos(θ) + j sin(θ)
j θ
ej θ + e−j θ
2
j θ
cos(θ) = Re[e ] =
sin(θ) = Im[e ] =
ej θ − e−j θ
2j
.
Polar to rectangular conversion

## Slide 16
Roots and powers of j
z 3 + 1 = 0 ⇒
3
k
z = −1 = e
j (2k+1)π
, k = 0, 1, 2
zk = ej (2k+1)π/3, k = 0, 1, 2
z0 = ej π/3,
z1 = ej π = −1,
z2 = ej (6−1)π/3 = ej 2πe−j π/3 = e−j π/3
0.5
1
30
210
60
240
90
270
120
300
150
330
180
0
0.5
1
30
210
60
240
90
270
120
300
150
33
180
Left: roots of z3 + 1 = 0. Right: integer powers of j , periodic of period 4, with period of {1, j ,− 1, − j }

## Slide 17
Trigonometric identities

## Slide 18: Phasors
ψ phase (rad)
Sinusoids and phasors
x (t) = A cos(Ω0t + ψ) − ∞ < t < ∞
A amplitude, Ω0 = 2πf0 frequency (rad/sec),
Phasor : X = Aej ψ, x (t) = Re[Xej Ω0t ]
sin
Ω0
cos
sin
Generation of sinusoids from phasors of a frequency Ω0 shown at initial position

## Slide 19
10
20
30
30
210
60
240
90
270
120
300
150
330
180
0
Phasor 1 + Phasor 2
20
10
30
210
240
90 30
60
270
120
300
150
330
180
0
0
0.02
0.04
0.06
0.08
0.1
0.12
0.14
0.16
0.18
0.2
−40
−20
0
40
20
Sum of phasors I1 = 10 ej 0 and I2 = 20 ej π/4 with the result in the top left and the corresponding sinusoid (right bottom).

## Slide 20: Phasors and systems
Eigenfunction property of LTI systems
Input: x (t) = Re[Xej Ω0t ], input phasor X = Aej θ
j Ω0t
Output: y (t) = Re[Ye ], output phasor Y = XH(j Ω0)
Steady–state response
Linear time-invariant system
Input
Output
x(t) = A cos(Ω0t + θ)
yss(t) = A|H(jΩ0)| cos(Ω0t + θ + ∠H(jΩ0))
Frequency response of system